## Slide 1: An Improved Public Unclonable Function Design for Xilinx FPGAs for Hardware Security 1st M.A.Sc Seminar
Presenter: Siva Prashanth B
Supervisor: Dr. Mohammed A. S. Khalid
Dr. Mitra Mirhasanni
Date: , 2018
University of Windsor
Department of Electrical and Computer Engineering

## Slide 2: Seminar Outline
Introduction
Problem Statement
Related Works
Research Goals and Strategy
Current Research Status
Summary
References

## Slide 3
INTRODUCTION:
Physical Unclonable Functions (PUFs) are digital circuits that produce unique signature bits based on process variations that occur in manufacturing process.
PUF’s eliminate the need to buy expensive cryptographic algorithm for security instead we can use the hardware itself as the security device.
No need to store the secret keys in digital memory such as SRAM and EEPROM which could be pervasive to many attacks.

## Slide 4: How does it work ??
A PUF is passed an input challenge C, and returns a response R.
R = f (C), where f (.) describes the input/output relations of the PUF.

## Slide 5: Why (PUF)s are important ?
PUF hardware uses simple digital circuits that are easy to
fabricate or can use structures within.
Consumes less power and area than EEPROM/RAM solutions.
Nonvolatile memory is more expensive to manufacture. EEPROMs require additional mask layers, and RAMs require an external always-on power source.

## Slide 6: Classification of PUF:
Weak PUF: Used For key storage. A weak PUF (also called as Physically Obfuscated PUF’s) has a very small range such that it can have collisions with one or other challenges that give the same response.
Strong PUF: Commonly used for authentication. Strong PUf’s have a large domain and supports a lot of CRP’s that means it can be used effectively and securely.

## Slide 7: Properties of PUF
Intra PUF Variation:
Its defined as the number for bits in a PUF response that change when the same challenge input is given to the PUF. Usually, this happens due to environmental variation and statistical noise.
Inter-PUF Variation:
Its defined as the number of bits in a PUF response that vary between different devices for the same challenges. This is due to differences in IC Fabrication. It’s the measure of the uniqueness

## Slide 8
PROBLEM STATEMENT:
Creating an efficient PUF model of an Anderson’s design for
Xilinx Virtex FPGA Boards.
Anderson’s PUF measures an intra-distance of roughly 90 bits.
it corresponds to an error of around 30% [2].
IP Protection by a low cost method for the Xilinx FPGA Boards.

## Slide 9: RELATED WORKS:
Anderson’s PUF:
a PUF circuit was designed using 2 LUTs, 2 carry chains and one F/F of the underlying architecture of 65nmVirtex 5 Xilinx FPGA.[1]
The PUF circuit consumes very little area (i.e) 2 slices so we can create a lot of combinations inside the FPGA.

## Slide 10: RESEARCH GOALS AND STRATEGY
Re-Design of Anderson’s PUF to avoid intra PUF variation.
Efficient Model of Anderson’s PUF Design changing the glitch value to 0 instead of 1 which leads to a robust design.
Designing an FSM based Hardware Trojan with the Anderson’s PUF.

## Slide 11: Re-Design of Anderson PUF
The analysis said that glitches of short duration are not enough to trigger the flip flop.
To overcome the Constant glitch problem, we have two solutions:
1) Measurement after a specific delay
2) A One-shot approach

## Slide 12: Measurement after specific delay
To latch the PUF output at a single point of time.
PUF response at a later point in time so that response is close to being uniformly distributed without the need for key extraction.
The results relate to sampling the PUF after .5 sec after power on, then using the response at a variety of times thereafter.

## Slide 13: One-shot approach:
We control the glitch width transitions between LUT0 and LUT1, increasing it so the probability that a glitch occurs at a preset input of flipflop is also increased.
This can be realised by adding an additional carry chain between the two LUT’s.

## Slide 14: Modification of the Anderson’s PUF Design by changing the glitch value from ‘1’ to ‘0’
This uses an Efficient model of the Anderson’s PUF.

## Slide 15: Experimental Results
Before : After:

## Slide 16: Hardware Trojan
A Hardware Trojan (HT) is a malicious modification of the circuitry of an integrated circuit. A Hardware Trojan is completely characterized by its physical representation and its behaviour.
This FSM needs to be hidden from attackers. Obfuscation technique will be used during this research based on re-simulating the FSM of the IP core with the added FSM to gather a flattened netlist.

## Slide 17
The binding FSM structure. The original states are shown in dark and the added states are shown in white on the STG of the added FSM. [3]

## Slide 18
Expected Implementation and Results:
The proposed Modified Anderson PUF and the binding FSM-Anderson IP protection method will be implemented on Xilinx FPGA using ISE tools.
To evaluate the effectiveness of the proposed binding method.
The area, timing and power overhead will be studied on the benchmark circuits.

## Slide 19: CURRENT RESEARCH STATUS
Got results for Modified Anderson’s puf with a change in glitch value.
Made a FSM based design for a simple multiplier based IP with a timebomb.
Got results for Re-Design of Andersons PUF.

## Slide 20: SUMMARY:
Thus PUF’s can act as a good low cost Hardware Protection for FPGA Devices.
They can be used for Anti - Counterfeiting, Anti-Cloning, Trusted Storage, Secure Payments, Machine to Machine and Device Cloud Authentication.
It can be used as a Time Bomb like making it to use it for evaluation period and later make the users pay for it for applying the response to the PUF.

## Slide 21: FUTURE RECOMMENDATIONS:
Investigation of whether the saturation effect itself is an intrinsic property of an FPGA device.
Analysing protection and detection techniques on ASIC’s instead of FPGAs.
Comparing the security strength of the proposed designs.

## Slide 22: REFERENCES:
[1] J.H Anderson. A PUF design for secure FPGA-based embedded systems. In ASP-DAC, pages 1-6, 2010.
[2] P. Grabher, D. Page and M. Wojcik. On the (re) design of an FPGA-based PUF.
[3] Amr Alanwar, Mona A. Aboelnaga, Yousra Alkabani, M. Watheq and Hassan Bedour. Dynamic FPGA Detection and Protection of Hardware Trojan: A Comparative Analysis.
[4] Masoud Rostami, Farinaz Koushanfar, and Ramesh KarriA Primer on Hardware Security:Models, Methods, and Metrics.
[5] Virtex-5 FPGA Data Sheet, Xilinx, Inc., San Jose, CA, 2007.
[6] M. Majzoobi, F. Koushanfar, and M. Potkonjak, “Techniques for design and implementation of secure reconfigurable PUFs,”ACM Trans. on Reconfigurable Technology and Systems, vol. 2,no. 1, pp. 1–33, 2009.

## Slide 23: QUESTIONS

## Slide 24: THANK YOU