## Slide 1: Acceleration of Matrix Decomposition and Machine Learning Algorithms on FPGA using Altera SDK for OpenCL 1st M.A.Sc Seminar
Presenter: Ryan Tang
Supervisor: Dr. Mohammed A. S. Khalid
Date: March 31, 2015
University of Windsor
Department of Electrical and Computer Engineering

## Slide 2: Seminar Outline
Introduction
  Problems
  Tool (AOCL)
Problem Statement
Related Works
Research Goals and Strategy
Current Research Status
Summary
References

## Slide 3: Introduction

## Slide 4: Introduction: Background on Matrix Decomposition Algorithms
Matrix decomposition methods decompose a matrix into the product of a number of matrices.
Time Complexity O(n3)
Applications:
  Solving of linear systems, finding matrix inverse, linear least squares method, etc.
  Statistics, Machine Learning, Radar Signal Processing, Simulations, Optimizations, etc.
Algorithms that this research will implement:
  LU decomposition, Cholesky decomposition, and QR decomposition.

## Slide 5: Introduction: Matrix Decomposition Algorithms Overview 1
LU decomposition:
  Decompose matrix A into lower triangular matrix L and upper triangular matrix U.
  The matrix must not be singular
  Method: Modified Gaussian Elimination (Doolittle/Crout)
  About 2/3n3 floating point operations
Cholesky decomposition:
  Decompose matrix A into lower triangular matrix L and upper triangular matrix LT.
  The matrix must be Hermitian positive semi-definite
  Method: Modified Gaussian Elimination (Cholesky/Crout)
  About 1/3n3 floating point operations

## Slide 6: Introduction: Matrix Decomposition Algorithms Overview 2
QR decomposition:
  Decompose matrix A into orthogonal matrix Q and upper (right) triangular matrix R.
  Method: Modified Gram-Schmidt / Givens / Householder
  About 2/3n3 floating point operations
Parallel forms of matrix decompositions:
  Blocked/Panel:
    Used for large matrices, applies blocked GEMM (matrix multiplication)
  Batched:
    Used for lots of smaller matrices, direct solving
Dense / Sparse:
  Using dense matrix only for this research

## Slide 7: Introduction: Background on Machine Learning Algorithms
Construct models based on training samples and use this model to make predictions when given new data
Classification of Learning Problems:
  Based on label given or not:
    Supervised learning, unsupervised learning etc.
  Based on expected result:
    Regression, Classification, Clustering etc.
Applications:
  Image recognition, pattern recognition, machine vision, data mining, autonomous vehicle etc.

## Slide 8: Introduction: Background on Machine Learning Algorithms cont.
Machine Learning Algorithms this research will implement:
  K-means
  Support Vector Machines (SVMs)
  K-nearest neighbors (K-NN)
Will only explorer classification problems for simplicity
Computationally intensive when problem / feature size is large

## Slide 9: Introduction: Machine Learning Algorithms Overview 1
K-means:
  Clustering algorithm, unsupervised learning
  Training:
    Step 1: Initialization: randomly assign location to k centroids
    Step 2: assign closest centroids to each training samples
    Step 3: update centroid locations using 2.
    Repeats steps 2 & 3 until converge
  Classifying:
    Class of test data = class of nearest centroid
  Can be used to detect / choose features for other learning algorithms

## Slide 10: Introduction: Machine Learning Algorithms Overview 2
SVM:
  Supervised learning, based on logistic regression
  Separates samples into different classes with a hyperplane
    Can be linear, polynomial, etc.
  Training:
    Use optimization algorithms such as sequential minimal optimization (SMO) or gradient descent to find hyperplane parameters that maximizes margins
K-NN:
  Instance-based Learning
    Training = remember training samples
  Classifying
    Class of test data = class of the k-nearest neighbors (with weight function)
  Require efficient data structure (kd-tree)

## Slide 11: Introduction: Background on FPGAs
Field Programmable Gate Array
  Reconfigurable logic, combined with hard logic
  Used in embedded system applications
Pros:
  Powerful and efficient computation devices
  More flexible and less development cost compare to ASIC
Cons:
  Difficult to program, require use of hardware description language (HDL) and extensive hardware knowledge
  Longer development time and higher cost compare to GPGPU/CPU

## Slide 12: Introduction: Background on High Level Synthesis
High Level Synthesis (HLS)
  Translates high level language such as C, C++ and SystemC to low level HDL such as Verilog and VHDL
Established HLS Tools
  Convert to RTL
    C to Silicon (Cadence)
    Catapult C (Mentor Graphics)
    Synphony C Compiler (Synopsis)
  Software Hardware Co-Design
    LegUp (University of Toronto)
    Vivado HLS (Xilinx)
    Impulse C (Impulse Accelerated)
  Special Language (BlueSpec)

## Slide 13: Introduction: Introducing Altera SDK for OpenCL
HLS tool that compiles High Level OpenCL to Verilog targeting Altera FPGAs
Architecture
  Host: C++ programs, manage resources and task
  Device: OpenCL computation kernels, executed on FPGA
How does it work
  Compile OpenCL to Verilog using AOC compiler and Qsys, then to device binary using Quartus II
  Compile C++ host to binary using GCC/Visual Studio
Targeting High performance Computing (HPC) and Embedded Applications
  Stratix V and Cyclone V FPGA support

## Slide 14: Introduction: Background on OpenCL
Open Computing Language based on C99
Industry standard language for parallel and high performance computing
Explicit parallelism
  task parallelism and data parallelism
Device support
  CPU, GPU, FPGA(new), DSP(new), heterogeneous
Vender support
  Intel, AMD, Nvidia, Altera, Apple, Xilinx(new), and more
Other Similar Solutions
  OpenACC, OpenMP, CUDA (for CPU and GPGPU only)

## Slide 15: Introduction: Comparisons
Altera OpenCL Cont.
  Advantages:
    Industry standard language
    Low development time and cost
    Streamlined design flow, expose power of FPGA to software engineers
    FPGA has lower power consumption
    Long life cycle (Don’t need to redesign the program for newer FPGAs)
    Allows heterogeneous computing
  Drawbacks
    High compilation resource cost and time
    In some case still requires hardware knowledge
    (Current generation) lower floating point capability to GPGPU
    Difficult to optimize / less transparent to debugging/profiling
    The optimization in code reduces portability

## Slide 16: Problem Statement

## Slide 17: Problem Statement
Parallel Computing using GPU and CPU is a well researched topic in the past and current decade
FPGA are powerful and flexible, but far less utilized in parallel computing due to difficulty to program and long development time
Altera SDK for OpenCL allows acceleration of algorithms on efficient customized hardware without extensive hardware knowledge

## Slide 18: Problem Statement (Cont.)
Can Altera SDK for OpenCL give FPGAs the capability to compete in parallel computing / HPC arena?
We would like to port parallel algorithms already efficiently implemented on CPU and GPU to FPGA and determine the effectiveness of the Altera SDK for OpenCL against established CPU and GPU platforms
Dense linear algebra and machine learning algorithms covers a few major types of parallel computing applications and are good starting points

## Slide 19: Related Works

## Slide 20: Related Works Matrix Decomposition Solution Overview
Standard Solution:
  LAPACK and related BLAS 3 based libraries:
    MKL (Intel CPU) [1]
    cuBLAS (Nvidia GPU) [2]
    MAGMA (heterogeneous) [3]
  LU Tested on i7-3740QM (45W) and K2000m (55W)
    MKL: 150 GFLOP/s Blocked;
    cuBLAS: 175 GFLOP/s Blocked; 226 GFLOP/s Batched
    MAGMA: 230 GFLOP/s Blocked;140 GFLOP/s Batched
    (All results are single precision)

## Slide 21: Related Works Matrix Decomposition on HPC
V. Volkov and J. Demmel presented an implementation of LU, QR and Cholesky decomposition on GPU (2008) [4]
  309 ~ 340 GFLOP/s SP on GTX 280 GPU+CPU
  70~75 GLOP/s SP on a Q6850 CPU
C. Cao et al. presented clMAGMA dense linear algebra library system (2014) [5]
  LU: 326 GFLOP/s DP on 7970 GPU + 6 core Phenom II
  Cholesky: 344 GFLOP/s DP on same hardware
  QR: 347 GFLOP/s DP on same hardware
  Speedup 5~6x versus CPU (MKL 11.1)

## Slide 22: Related Works Matrix Decomposition on FPGA
W. Zhang developed a Verilog hand coded FPGA based direct linear system solver in master thesis (2008) [6]
  LU: 47 GFLOP/s on Stratix III SL340 at 20 W
    72x DSP (288x 18x18 Mul);
  Was more power efficient than MKL on Xeon 5160
Altera Corporation presented DSP builder implemented Cholesky and QR on small matrices for radar DSP [7]
  Cholesky: 92 GFLOP/s SP 360x360 matrices on Stratix V D5
    1590x DSP (3180x 18x18 Mul); 2014/39MBits M20K
  QR: 162 GFLOP/s SP 250x400 matrices on same hardware
  Concluded that FPGAs better suited for smaller data size

## Slide 23: Related Works Machine Learning K-means
M. Zechner and M. Granitzer presented CUDA implementation of K-means (2009) [8]
  36 GFLOP/s on 9600 GT GPU, claim 14x over CPU
O. Segal et al. presented work on expending Java programming framework APARAPI to support Altera OpenCL SDK and Results of running Nbody Simulation and K-Means (2014) [9]
  Implemented on Altera FPGA
  5.2x-7x speed increase in K-Means vs. CPU

## Slide 24: Related Works Machine Learning SVM
Austin Carpenter presented an CUDA implementation of Support Vector Machines. (2009) [10]
  12-73x faster learning then LIBSVM CPU solver when using GTX 260 GPU
  22-172x faster perdition then LIBSVM CPU solver with the same hardware
S. Wang et al. presented and Least Squares Support Vector Machine on Xilinx Virtex V FPGA (2011) [11]
  6~218x over a Xeon CPU implementation when training sample is greater than 256

## Slide 25: Related Works Machine Learning K-Nearest Neighbors
H. Hussain et al. presented an dynamically reconfigurable kNN classifier implementation on Xilinx Virtex 4 FPGA (2012) [12]
  76x ~ 68x faster than Matlab implementation on Pentium Dual-Core E5300
I. Stamoulias and E. Manolakos presented implementation of kNN classifier on Xilinx Virtex 5 FPGAs (2013) [13]
  Was 10 times slower then an earlier (2008) GPU implementation at large problem size but was considerably more power efficient
  Quoted GPU implementation claimed to be 100x faster than CPU of its time

## Slide 26: Research Goals and Strategy

## Slide 27: Research Goals and Strategy Goals
To implement LU, Cholesky and QR decomposition methods on FPGA using Altera SDK for OpenCL.
To implement regressions, SVM, k-means, and KNN machine learning algorithms on FPGA FPGA using Altera SDK for OpenCL.
To implement the stated algorithms on CPU and GPU using highly efficient library such as cuBLAS, MAGMA, MKL, GPUMLib
Compare performance, power efficiency and numerical accuracy.
Use the data obtained to evaluate the capability of Altera SDK for OpenCL.

## Slide 28: Research Goals and Strategy Strategy
  Phase 1:
  Implement the algorithm on CPU without parallelism. Study the algorithms and determine the best way to implement them on parallel platforms
  Phase 2:
  Implement the algorithms on FPGA using Altera SDK for OpenCL
  Phase 3:
  Implement the algorithms on CPU and GPU using available libraries and compare performance, power efficiency and numerical accuracy with FPGA implementations.

## Slide 29: Current Research Status
Completed
  Matrix Decomposition
    Study the algorithms
    Implementation of Blocked and Batch LU decomposition on FPGA, GPU and CPU using Altera OpenCL, CUDA SDK and MKL
Currently In progress
  Matrix Decomposition
    Implementation of Cholesky decomposition on FPGA, GPU and CPU and compare performance
    Investigate the reason for low performance of LU on FPGA
  Machine Learning
    Taking machine learning open course
    Implementing un-optimized k-means and gradient descent algorithm sequentially on CPU using C++

## Slide 30: Summary
Matrix decomposition and machine learning algorithms are computationally intensive when problem size is large.
Currently fairly good software solutions exist to accelerate said algorithms using CPU and GPU.
HLS tools such as Altera SDK for OpenCL allows acceleration of algorithms using FPGA much easier then before.
This research attempts to find out if it is possible achieve higher performance with less power consumption using Altera SDK for OpenCL on FPGA than existing libraries on CPUs or GPUs.

## Slide 31: References
[1] Intel Corporation “Intel® Math Kernel Library (Intel® MKL),” [Online]. Available: https://software.intel.com/en-us/intel-mkl
[2] NVIDIA Corporation, “cuBLAS,” [Online]. Available: https://developer.nvidia.com/cuBLAS
[3] Innovative Computing Laboratory, “Matrix Algebra on GPU and Multicore Architecture,” [Online]. Available: http://icl.utk.edu/magma/
[4] Volkov, V.; Demmel, J.W., "Benchmarking GPUs to tune dense linear algebra," International Conference for High Performance Computing, Networking, Storage and Analysis, 2008., pp.1,11, 15-21 Nov. 2008
[5] Cao, C. et al., “clMAGMA: high performance dense linear algebra with OpenCL,” In Proceedings of the International Workshop on OpenCL 2013 & 2014., Article 1, 2014
[6] Wei Zhang, Portable and Scalable FPGA-Based Acceleration of a Direct Linear System Solver, MASc thesis, University of Toronto, 2008

## Slide 32: References (Cont.)
[7] Altera Corporation, Radar Processing: FPGAs or GPUs?, May 2013. [Online]. Available: https://www.altera.com/en_US/pdfs/literature/wp/wp-01197-radar-fpga-or-gpu.pdf
[8] Zechner, M.; Granitzer, M., "Accelerating K-Means on the Graphics Processor via CUDA," Intensive Applications and Services, 2009. INTENSIVE '09. First International Conference on , vol., no., pp.7,15, 20-25 April 2009
[9] Segal, O.; Margala, M.; Chalamalasetti, S.R.; Wright, M., "High level programming framework for FPGAs in the data center," Field Programmable Logic and Applications (FPL), 2014 24th International Conference on , vol., no., pp.1,4, 2-4 Sept. 2014
[10] A. Carpenter, "cusvm: A cuda implementation of support vector classification and regression, " 2009. [Online]. Available: http://patternsonascreen.net/cuSVM.html.

## Slide 33: References (Cont.)
[11] Shaojun Wang; Yu Peng; Guangquan Zhao; Xiyuan Peng, "Accelerating on-line training of LS-SVM with run-time reconfiguration," Field-Programmable Technology (FPT), 2011 International Conference on , vol., no., pp.1,6, 12-14 Dec. 2011
[12] Hussain, H.M.; Benkrid, K.; Seker, H., "An adaptive implementation of a dynamically reconfigurable K-nearest neighbour classifier on FPGA," NASA/ESA Conference on Adaptive Hardware and Systems (AHS), 2012., pp.205,212, 25-28 June 2012
[13] Ioannis Stamoulias and Elias S. Manolakos. “Parallel architectures for the kNN classifier -- design of soft IP cores and FPGA implementations,” ACM Trans. Embed. Comput. Syst. 13, 2, Article 22 Sept. 2013

## Slide 34: Thank you!

## Slide 35: Appendix Background on Accelerator Hardware
Accelerator Card Designed for Altera OpenCL
  DE5-net (Terasic)
  PCIe-385N (Nallatech)
Stratix V A7 FPGA
  622K logic elements
  939K registers, 50 Mbits M20K block memory
  256 DSP (27x27 Multiplier) floating point blocks
  ≤25W typically (Nallatech)
Include 4~8GB of DDR3 800MHz RAM
Include board support package (BSP)
  Vendor implemented driver, libraries and memory control logic.

## Slide 36: Appendix Gaussian Elimination
From Numerical
Methods for
Engineers 6th
P249

## Slide 37: Appendix LU Decomposition

## Slide 38: Appendix Cholesky Decomposition

## Slide 39: Appendix Cholesky Decomposition Blocked
Image
From
www.netlib.org
Maker of
LAPACK

## Slide 40: Appendix QR Decomposition

## Slide 41: Appendix K-means
From CS 229 Lecture Notes

## Slide 42: Appendix Support Vector Machine

## Slide 43: Appendix K-Nearest Neighbors
Form machlearning-001 course notes